## Slide 1
Multilayer Switches
High-performance networking that bridges switching and routing — built for the demands of modern enterprise infrastructure.
ENTERPRISE NETWORKING
LAYER 2 & LAYER 3
Made by Stuti Shah
SYCS_53
PRN: 125BTCS1057

## Slide 2
What Is a Multilayer Switch?
A multilayer switch (MLS) is an advanced networking device that combines the functions of a traditional Layer 2 switch with Layer 3 routing capabilities — all within a single hardware platform.
Layer 2 Switching
Forwards frames using MAC addresses at wire speed
Layer 3 Routing
Routes packets between VLANs using IP addresses
Unified Platform
Eliminates the need for a separate router in many designs

## Slide 3
OSI Layer Operation
Multilayer switches operate intelligently across two critical layers of the OSI model, enabling both fast switching and smart routing decisions.
Layer 2 — Data Link
Reads MAC addresses to forward Ethernet frames within a broadcast domain. Builds and references a MAC address table for fast lookups.
Layer 3 — Network
Inspects IP headers to route packets between subnets or VLANs. Maintains a routing table for intelligent next-hop decisions.
Hardware Forwarding
Both layers leverage ASICs (Application-Specific Integrated Circuits) for near-wire-speed packet processing with minimal CPU overhead.

## Slide 4
How It Works: The Forwarding Pipeline
ASIC Forwarding
IP Lookup
MAC Lookup
Frame Arrives
By processing packets in hardware via ASICs rather than software, multilayer switches achieve sub-microsecond forwarding decisions — far faster than traditional router-based designs.

## Slide 5
Key Features
Inter-VLAN Routing
Routes traffic between VLANs without a separate router
High-Speed Routing
ASIC-based forwarding delivers near-wire-speed performance
ACLs & Security
Access Control Lists filter traffic at line rate for granular security
QoS
Classifies and prioritizes traffic to guarantee performance for critical applications

## Slide 6
Advantages Over Traditional Routers
Faster Than Routers
Hardware-based ASIC forwarding outperforms software-based routing CPUs, delivering significantly lower latency.
Scalability
Supports hundreds of VLANs and thousands of MAC addresses, scaling gracefully with enterprise growth.
Reduced Congestion
Local routing keeps inter-VLAN traffic on the switch fabric, eliminating hair-pinning through an external router.

## Slide 7
Limitations to Consider
Multilayer switches are powerful, but they come with trade-offs that network architects must evaluate.
💰 Higher Cost
MLS devices carry a premium over basic Layer 2 switches due to advanced hardware and licensing.
⚙️ Configuration Complexity
Requires expertise in routing protocols, VLAN design, ACLs, and QoS policies.
🌐 Limited WAN Functionality
MLS devices are optimized for LAN environments and lack advanced WAN features like MPLS or SD-WAN.
📚 Learning Curve
Teams must be trained on both switching and routing concepts to manage these devices effectively.

## Slide 8
Real-World Applications
🏢 Enterprise LANs
Core and distribution layer switching for large office networks
🖥️ Data Centers
High-density, low-latency interconnect for server clusters
🎓 Universities & Campuses
Segmented networks for students, faculty, and research labs
🏭 Industrial Networks
Reliable, segmented infrastructure for manufacturing and OT environments
SDG 9 — Industry, Innovation & Infrastructure: Multilayer switches directly support resilient, scalable network infrastructure — a cornerstone of modern innovation and sustainable industrialization.

## Slide 9
Multilayer Switch vs. Traditional Layer 2 Switch
Understanding the differences helps you choose the right device for each network layer.
Feature
Layer 2 Switch
Multilayer Switch
OSI Layers
Layer 2 only
Layer 2 + Layer 3
Routing Capability
None
Full IP routing
Inter-VLAN Routing
Requires external router
Built-in
Forwarding Speed
Fast (MAC-based)
Very fast (ASIC-based)
ACL & QoS Support
Limited
Advanced
Cost
Lower
Higher
Best Use Case
Access layer
Core / Distribution

## Slide 10
Key Takeaways
Unified Performance
Multilayer switches deliver hardware-accelerated routing and switching in a single device, eliminating bottlenecks.
Enterprise-Ready
With Inter-VLAN routing, QoS, and ACLs, MLS devices are purpose-built for scalable, secure campus and data center networks.
Strategic Investment
Despite higher cost and complexity, the performance gains and operational simplicity make MLS the right choice for core network layers.